## Slide 1
BIONIC ARM
SIMULATION & CODE IMPLEMENTATION
Mentored by: Dr. Mitresh Kumar Verma
Indian Institute of Technology (BHU) Varanasi

## Slide 2
  Modern bionic arms offer improved dexterity over traditional passive prosthetics
  Simulation enables safe, cost-effective testing of control algorithms and mechanical designs
  Builds on research in sensor gloves and prosthetic control systems
  Allows for iterative design and validation before committing to hardware
  Addresses the need for more natural, user-friendly assistive technology
PROJECT MOTIVATION & BACKGROUND

## Slide 3
  Aims to design a prosthetic limb controlled via a wearable glove interface
  Project structured in two phases:
    Phase 1: Simulation using PyBullet to create and validate a virtual bionic arm
    Phase 2: Planned physical prototyping based on simulation results
  Virtual model includes palm, fingers, and forearm with realistic joint constraints
  Grasping and pinching functions successfully demonstrated in simulation
  Sets the foundation for real-time sensor glove integration and hardware fabrication
PROJECT OVERVIEW

## Slide 4
  Built on PyBullet physics engine for accurate rigid-body dynamics and collision detection
  Environment setup includes:
    Ground plane as the base surface
    Manipulable object (sphere or cube) for grasping and pinching tests
    18-joint bionic hand model anchored in space (simulating a prosthetic)
  Self-collision detection enabled for realistic finger interactions
  Visual, interactive simulation provides immediate feedback for code and design changes
SIMULATION ENVIRONMENT

## Slide 5
  Hand model structured with 18 joints for high dexterity:
    2 forearm tilt joints (for arm orientation)
    1 wrist joint (rotation)
    3 joints per finger (index, middle, ring, pinky) for base, middle, and tip movement
    3 thumb joints (lateral base and two curl joints)
  Hierarchical joint mapping allows coordinated and individual finger control
  Joint organization mimics human hand anatomy for natural motion
  Helper functions in code enable easy access and control of finger joints
HAND MODEL & JOINT STRUCTURE

## Slide 6
HAND MODEL & JOINT STRUCTURE

## Slide 7
  Extensive keyboard mapping for intuitive control:
    Keys assigned for forearm, wrist, individual fingers, and thumb movements
    Dedicated keys for synchronized grasping and pinching actions
  Keyboard events polled at simulation rate (240 Hz) for real-time responsiveness
  Interface supports thorough testing of all control algorithms and gestures
  Code structured to allow future integration with sensor glove inputs
USER INTERFACE & KEYBOARD MAPPING

## Slide 8
KEYBOARD MAPPING

## Slide 9
  Position control: Target positions for each joint incrementally adjusted based on user input
  Step sizes for joint movement tuned for different sensitivity needs (e.g., smaller for fingertips)
  Every joint link has an inbuilt closed loop servo motor which responds to the desired position given as input.
  Friction parameters set for each joint and object to prevent slippage during manipulation
CONTROL SYSTEM IMPLEMENTATION

## Slide 10
  Synchronized grasping: All fingers close together using a grasp_state variable (0.0 = open, 1.0 = closed)
  Precision pinching: Index finger and thumb coordinated for fine object manipulation with pinch_state
  Closed positions for each joint calibrated for effective grasp and pinch
  Incremental updates to grasp/pinch state enable smooth, gradual transitions
  Functions implemented in code allow for both individual and combined gestures
GRASPING & PINCHING FUNCTIONS

## Slide 11
PICKING UP AN OBJECT

## Slide 12
  Future plans include:
    Developing a sensor glove with flex sensors and Arduino Nano
    Calibration of sensor data to joint angles for real-time control
    Physical prototype fabrication based on validated simulation model
  Modular codebase designed for easy extension and adaptation
FUTURE WORK

## Slide 13
QUESTIONS
&
ANSWERS

## Slide 14
THANK
YOU
Aayush | Abhinav Jaiswal | IIT BHU | 2025